Large Pulley (10mmshaft)

// Belt pulley is http://www.thingiverse.com/thing:3104 by GilesBathgate
// GPLV3
// Made parametric by droftarts September 2011
// extra mods by triffid_hunter

/**
* @name Pulley
* @category Printed
* @using 1 x m3 nut, normal or nyloc
* @using 1 x m3x10 set screw or 1 x m3x8 grub screw
*/

module pulley()
{

// tuneable constants

m3_dia = 4.2; // 3mm hole diameter
m3_nut_hex = 1; // 1 for hex, 0 for square nut
m3_nut_flats = 6.5; // normal M3 hex nut exact width = 5.5
m3_nut_depth = 2.9; // normal M3 hex nut exact depth = 2.4, nyloc = 4
motor_shaft = 9.6; // NEMA17 motor shaft exact diameter = 5

retainer = 1; // Belt retainer end, 1 for Yes, 0 for No
idler = 0; // 0 = No, 1 = Yes; fills in dish of retainer, if required
retainer_ht = 4; // height of retainer flange over pulley, standard = 4. Indented into pulley by 2mm.

teeth = 12; // Number of teeth, standard Mendel = 8
tooth_width = 2.5; // width of base of tooth, exact size for T5 = 2.65, XL = 2.6124. Increase to improve fit.
tooth_angle = 60; // angle of tooth sides, exact angle for T5 = 40, XL = 50
tooth_height = 1.4; // height of tooth, exact size for T5 = 1.2, XL = 1.3 Increase to improve fit.

pulley_t_ht = 9; // length of toothed part of pulley, standard = 12
pulley_b_ht = 9; // 8 pulley base height, standard = 8
pulley_b_dia = 24; // pulley base diameter, standard = 20
no_of_nuts = 1; // number of captive nuts required, standard = 1
nut_angle = 90; // angle between nuts, standard = 90
nut_shaft_distance = 1.2; // distance between inner face of nut and shaft. standard = 1. Can be negative if your motor has D-shaft or filed flat. Do not set to zero or openscad will make a bad STL

// BELT SELECTION - uncomment preferred belt type
belt_type = "VAC";
teeth_dia = ((1.41 * pow(teeth,1.08)) / (0.84 + pow(teeth,1.08))) * teeth;

//belt_type = "T5";
//teeth_dia = ((1.591 * pow(teeth,1.064)) / (0.6523 + pow(teeth,1.064))) * teeth;

//belt_type = "XL";
//teeth_dia = ((1.617 * pow(teeth,1.021)) / (0.339 + pow(teeth,1.021))) * teeth;

echo (str("Belt type = ",belt_type,"; number of teeth = ",teeth,"; teeth diameter = ",teeth_dia,"mm"));

// calculated constants

nut_elevation = pulley_b_ht/2;
m3_nut_points = 2*((m3_nut_flats/2)/cos(30)); // This is needed for the nut trap

// Modules

module spur()
{
linear_extrude(height=pulley_t_ht+2) polygon([[0,-(tooth_width/2)],[0,(tooth_width/2)],[-tooth_height,((tooth_width/2)-(tan(tooth_angle/2)*tooth_height))],[-tooth_height,-((tooth_width/2)-(tan(tooth_angle/2)*tooth_height))]],[[0,1,2,3,0]]);
}

module retainer()
{
rotate_extrude($fn=teeth*4) translate([teeth_dia/2-2.5,0,0])
polygon([[0,0],[1,0],[retainer_ht , retainer_ht - 1],[retainer_ht , retainer_ht],[retainer_ht-2 , retainer_ht],[0,2]],[[0,1,2,3,4,5,0]]);
}

// Main

difference()
{
union()
{
//base

if ( pulley_b_ht < 2 ) { echo ("CAN'T DRAW PULLEY BASE, HEIGHT LESS THAN 2!!!"); } else {
rotate_extrude($fn=pulley_b_dia*2)
{
square([pulley_b_dia/2-1,pulley_b_ht]);
square([pulley_b_dia/2,pulley_b_ht-1]);
translate([pulley_b_dia/2-1,pulley_b_ht-1]) circle(1);
}
}

difference()
{
//shaft - diameter is outside diameter of pulley
translate([0,0,pulley_b_ht]) rotate ([0,0,360/(teeth*4)]) cylinder(r=teeth_dia/2,h=pulley_t_ht, $fn=teeth*2);

//teeth - cut out of shaft
for(i=[1:teeth]) rotate([0,0,i*(360/teeth)])
translate([teeth_dia/2,0,pulley_b_ht-1]) spur();
}
//belt retainer end
if ( retainer > 0 ) {translate ([0,0,pulley_b_ht + pulley_t_ht -2]) retainer();
if ( idler > 0 ) {translate ([0,0,pulley_b_ht + pulley_t_ht]) cylinder(r1=teeth_dia/2-1,r2=(teeth_dia/2-2) + (retainer_ht-2),h=retainer_ht-2,$fn=teeth*4);}}

}
//hole for motor shaft
translate([0,0,-1])cylinder(r=motor_shaft/2,h=pulley_b_ht + pulley_t_ht + (retainer_ht),$fn=motor_shaft*4);
//captive nut and grub screw holes

if ( pulley_b_ht < m3_nut_flats ) { echo ("CAN'T DRAW CAPTIVE NUTS, HEIGHT LESS THAN NUT DIAMETER!!!"); } else {
if ( (pulley_b_dia - motor_shaft)/2 < m3_nut_depth + 3 ) { echo ("CAN'T DRAW CAPTIVE NUTS, DIAMETER TOO SMALL FOR NUT DEPTH!!!"); } else {

for(j=[1:no_of_nuts]) rotate([0,0,j*nut_angle])
translate([0,0,nut_elevation])rotate([90,0,0])

union()
{
//entrance
translate([0,-pulley_b_ht/4-0.5,motor_shaft/2+m3_nut_depth/2+nut_shaft_distance]) cube([m3_nut_flats,pulley_b_ht/2+1,m3_nut_depth],center=true);

//nut
if ( m3_nut_hex > 0 )
{
// hex nut
translate([0,0.25,motor_shaft/2+m3_nut_depth/2+nut_shaft_distance]) rotate([0,0,30]) cylinder(r=m3_nut_points/2,h=m3_nut_depth,center=true,$fn=6);
} else {
// square nut
translate([0,0.25,motor_shaft/2+m3_nut_depth/2+nut_shaft_distance]) cube([m3_nut_flats,m3_nut_flats,m3_nut_depth],center=true);
}

//grub screw hole
rotate([0,0,22.5])cylinder(r=m3_dia/2,h=pulley_b_dia/2+1,$fn=8);
}
}}
}
}

pulley();

Small Pulley
// Belt pulley is http://www.thingiverse.com/thing:3104 by GilesBathgate
// GPLV3
// Made parametric by droftarts September 2011
// extra mods by triffid_hunter

/**
* @name Pulley
* @category Printed
* @using 1 x m3 nut, normal or nyloc
* @using 1 x m3x10 set screw or 1 x m3x8 grub screw
*/

module pulley()
{

// tuneable constants

m3_dia = 4.2; // 3mm hole diameter
m3_nut_hex = 1; // 1 for hex, 0 for square nut
m3_nut_flats = 6.5; // normal M3 hex nut exact width = 5.5
m3_nut_depth = 3.2; // normal M3 hex nut exact depth = 2.4, nyloc = 4
motor_shaft = 6.6; // NEMA17 motor shaft exact diameter = 5

retainer = 1; // Belt retainer end, 1 for Yes, 0 for No
idler = 0; // 0 = No, 1 = Yes; fills in dish of retainer, if required
retainer_ht = 4; // height of retainer flange over pulley, standard = 4. Indented into pulley by 2mm.

teeth = 9; // Number of teeth, standard Mendel = 8
tooth_width = 2.5; // width of base of tooth, exact size for T5 = 2.65, XL = 2.6124. Increase to improve fit.
tooth_angle = 60; // angle of tooth sides, exact angle for T5 = 40, XL = 50
tooth_height = 1.4; // height of tooth, exact size for T5 = 1.2, XL = 1.3 Increase to improve fit.

pulley_t_ht = 9; // length of toothed part of pulley, standard = 12
pulley_b_ht = 9; // 8 pulley base height, standard = 8
pulley_b_dia = 20.6; // pulley base diameter, standard = 20
no_of_nuts = 1; // number of captive nuts required, standard = 1
nut_angle = 90; // angle between nuts, standard = 90
nut_shaft_distance = 1.4; // distance between inner face of nut and shaft. standard = 1. Can be negative if your motor has D-shaft or filed flat. Do not set to zero or openscad will make a bad STL

// BELT SELECTION - uncomment preferred belt type
belt_type = "VAC";
teeth_dia = ((1.41 * pow(teeth,1.08)) / (0.84 + pow(teeth,1.08))) * teeth;

//belt_type = "T5";
//teeth_dia = ((1.591 * pow(teeth,1.064)) / (0.6523 + pow(teeth,1.064))) * teeth;

//belt_type = "XL";
//teeth_dia = ((1.617 * pow(teeth,1.021)) / (0.339 + pow(teeth,1.021))) * teeth;

echo (str("Belt type = ",belt_type,"; number of teeth = ",teeth,"; teeth diameter = ",teeth_dia,"mm"));

// calculated constants

nut_elevation = pulley_b_ht/2;
m3_nut_points = 2*((m3_nut_flats/2)/cos(30)); // This is needed for the nut trap

// Modules

module spur()
{
linear_extrude(height=pulley_t_ht+2) polygon([[0,-(tooth_width/2)],[0,(tooth_width/2)],[-tooth_height,((tooth_width/2)-(tan(tooth_angle/2)*tooth_height))],[-tooth_height,-((tooth_width/2)-(tan(tooth_angle/2)*tooth_height))]],[[0,1,2,3,0]]);
}

module retainer()
{
rotate_extrude($fn=teeth*4) translate([teeth_dia/2-2.5,0,0])
polygon([[0,0],[1,0],[retainer_ht , retainer_ht - 1],[retainer_ht , retainer_ht],[retainer_ht-2 , retainer_ht],[0,2]],[[0,1,2,3,4,5,0]]);
}

// Main

difference()
{
union()
{
//base

if ( pulley_b_ht < 2 ) { echo ("CAN'T DRAW PULLEY BASE, HEIGHT LESS THAN 2!!!"); } else {
rotate_extrude($fn=pulley_b_dia*2)
{
square([pulley_b_dia/2-1,pulley_b_ht]);
square([pulley_b_dia/2,pulley_b_ht-1]);
translate([pulley_b_dia/2-1,pulley_b_ht-1]) circle(1);
}
}

difference()
{
//shaft - diameter is outside diameter of pulley
translate([0,0,pulley_b_ht]) rotate ([0,0,360/(teeth*4)]) cylinder(r=teeth_dia/2,h=pulley_t_ht, $fn=teeth*2);

//teeth - cut out of shaft
for(i=[1:teeth]) rotate([0,0,i*(360/teeth)])
translate([teeth_dia/2,0,pulley_b_ht-1]) spur();
}
//belt retainer end
if ( retainer > 0 ) {translate ([0,0,pulley_b_ht + pulley_t_ht -2]) retainer();
if ( idler > 0 ) {translate ([0,0,pulley_b_ht + pulley_t_ht]) cylinder(r1=teeth_dia/2-1,r2=(teeth_dia/2-2) + (retainer_ht-2),h=retainer_ht-2,$fn=teeth*4);}}

}
//hole for motor shaft
translate([0,0,-1])cylinder(r=motor_shaft/2,h=pulley_b_ht + pulley_t_ht + (retainer_ht),$fn=motor_shaft*4);
//captive nut and grub screw holes

if ( pulley_b_ht < m3_nut_flats ) { echo ("CAN'T DRAW CAPTIVE NUTS, HEIGHT LESS THAN NUT DIAMETER!!!"); } else {
if ( (pulley_b_dia - motor_shaft)/2 < m3_nut_depth + 3 ) { echo ("CAN'T DRAW CAPTIVE NUTS, DIAMETER TOO SMALL FOR NUT DEPTH!!!"); } else {

for(j=[1:no_of_nuts]) rotate([0,0,j*nut_angle])
translate([0,0,nut_elevation])rotate([90,0,0])

union()
{
//entrance
translate([0,-pulley_b_ht/4-0.5,motor_shaft/2+m3_nut_depth/2+nut_shaft_distance]) cube([m3_nut_flats,pulley_b_ht/2+1,m3_nut_depth],center=true);

//nut
if ( m3_nut_hex > 0 )
{
// hex nut
translate([0,0.25,motor_shaft/2+m3_nut_depth/2+nut_shaft_distance]) rotate([0,0,30]) cylinder(r=m3_nut_points/2,h=m3_nut_depth,center=true,$fn=6);
} else {
// square nut
translate([0,0.25,motor_shaft/2+m3_nut_depth/2+nut_shaft_distance]) cube([m3_nut_flats,m3_nut_flats,m3_nut_depth],center=true);
}

//grub screw hole
rotate([0,0,22.5])cylinder(r=m3_dia/2,h=pulley_b_dia/2+1,$fn=8);
}
}}
}
}

pulley();

Arduino Code:
// Using dual 2Amp motor driver DFRobot part # DR10002
// A and B are coils on Shuttle Altitude stepper motor
// MA(MB) enables the A(B) Coil and DA(DB) sets polarity
//
// Two analog voltages out (using PWM) on pins 3 and 9
// adjust the speeds of the Space Station and Shuttle resp.
//
// Space station speed is constant and slow
// Shuttle speed is inversely proportional to altitude
// and set to match Station velocity at the same altitude.
//
// Pin assignment

#define DA 7
#define MA 8
#define DB 5
#define MB 6

#define CW 10 // Forward
#define CCW 11 // Reverse
#define LOW_LIMIT_SWITCH 12 // Limit switch

#define STATION 3
#define SHUTTLE 9

#define VOLTS_TO_PWM(v) ( int ((v*255.0)/4.86) )
#define speed(p,v) analogWrite(p,VOLTS_TO_PWM(v))

#define NUM_SPEEDS 20
double speeds[NUM_SPEEDS] = {1.20,1.25,1.30,1.40,1.50,1.65,1.80,2.00,2.20,2.30,
        2.40,2.45,2.55,2.60,2.70,2.80,2.90,3.00,3.05,3.10};
int stationspeed;
int shuttlespeed;
int cntr;

#define MAX_HEIGHT 9000 // Don't go higher than this
int height;

boolean toggle;

// If we always stop as A -> 0 (and all other settings are zero)
// and and always start with A -> 1 (when all other settings are zero)
// there will be no gliches in the phase.

#define STEPS 8
#define REV(s) (s+1)%STEPS

const int dir_pin[STEPS] = {DA, DB, DB, DA, DA, DB, DB, DA };
const int dir_value[STEPS] = { 0, 1, 0, 0, 1, 0, 1, 1 };
const int enable_pin[STEPS] = {MA, MB, MB, MA, MA, MB, MB, MA };
const int enable_value[STEPS]= { 1, 0, 1, 0, 1, 0, 1, 0 };

void MOTOR(int i) {
digitalWrite(dir_pin[i],dir_value[i]);
digitalWrite(enable_pin[i],enable_value[i]);
//Serial.print(dir_pin[i]);Serial.print(" "),Serial.println(enable_pin[i]);
delay(2);
}

// Forward keeps track of the shuttle height

void forward(int count) {
Serial.println("forward");
while(count-- and height < MAX_HEIGHT) {
for(int i=STEPS-1; i>-1; i--) MOTOR(REV(i));
height += 1;
}
//	digitalWrite(DB,1);
        digitalWrite(MB,0);
        digitalWrite(MA,0);
}

// Reverse checks the lower limit switch (and adjusts the height value)

void reverse(int count) {
Serial.println("reverse");
while(count-- and digitalRead(LOW_LIMIT_SWITCH) ) {
for(int i=0; i<STEPS; i++) MOTOR(i);
if (height > 0) height -= 1;
}
//	digitalWrite(DA,1);
digitalWrite(MA,0);
digitalWrite(MB,0);
}

void flashLed () {
  // Turn the led on and off
  digitalWrite(LED_BUILTIN,toggle);
  toggle = !toggle;
}

void setup() {
  Serial.begin(9600);
  for (int i=2; i<6; i++) {
    pinMode(i,OUTPUT);
    digitalWrite(i,0);
  }
  pinMode(LED_BUILTIN,OUTPUT);
  toggle = true;
  pinMode(CW, INPUT_PULLUP);
  pinMode(CCW, INPUT_PULLUP);
  pinMode(LOW_LIMIT_SWITCH,INPUT_PULLUP);

  // Reverse the motor until it triggers the limit switch
  Serial.print("LLSW ");
  Serial.println(digitalRead(LOW_LIMIT_SWITCH));
  while (digitalRead(LOW_LIMIT_SWITCH)) {
Serial.println("reversing");
reverse(20);
delay(1);
  }

  height = 0;
  cntr = 0;
  shuttlespeed = 0;
  stationspeed = 19;
  speed(SHUTTLE, 1.3);
  Serial.println(VOLTS_TO_PWM(1.3));
  speed(STATION, 2.4);
  Serial.println(VOLTS_TO_PWM(2.4));
  Serial.println(VOLTS_TO_PWM(3.0));
}

void loop() {
  delay(1);
// flashLed();
  // Rotate the motor when a single button is pressed
  if (digitalRead(CCW) and !digitalRead(CW)) reverse(20);
  if (!digitalRead(CCW) and digitalRead(CW)) forward(20);
  if ((cntr++ % 5000) == 0)
Serial.println(height);
}